## Slide 1
DDJ-1000 Traktor mapping installation
This work requires the “BOME Midi translator Pro” third-party software
Steps are first explained, then shown via screenshots. Do not skip any step!
See also the installation FAQ (on a separate pdf file).

## Slide 2
Step #0
CONFIRM THAT REKORDBOX PERFORMANCE MODE WORKS PROPERLY IN YOUR SYSTEM!!
Driver Download: https://www.pioneerdj.com/en/support/software/controller/ddj-1000/#drivers
Firmware download: https://www.pioneerdj.com/en/support/software/controller/ddj-1000/#firmware-update
Rekordbox DJ download: https://rekordbox.com/en/

## Slide 3
Step #1
BOME TRIAL: INSTALLATION do not skip any step!

## Slide 4
BOME SOFTWARE INSTALLATION:
  Download and install the BOME trial from https://www.bome.com/products/miditranslator#downloads
MAC-OS SECURITY ENABLE (see page 40 of the BOME manual):
  macOS 10.9 and later:
    System Preferences → Security & Privacy → Privacy → Accessibility -> Add “BOME”
  macOS 10.8 and earlier:
    System Preferences → Universal Access → check 'access for assistive devices‘
  More info: https://www.maketecheasier.com/macos-security-privacy-permissions/

## Slide 5
macOS security:

## Slide 6
Step #2
MAP FOR BOME: INSTALLATION do not skip any step!

## Slide 7
PRELIMINARIES:
  Stop Rekordbox
  Stop Traktor
  Expand all files in the zip file
  Connect the USB cable
  Turn on your DDJ-1000
INSTALLING BOME MAPPING:
  Open BOME. DO NOT RUN TRAKTOR!
  Settings: Import the settings file
    Method: menu View; settings; export/import; import; select BMTS file
  Mapping: load the mapping file
    Method: Click menu File; Open; select BMTP file
  Do not mix up the Settings file with the Mapping file!
Beware!

## Slide 8
BOME: import settings file (BMTS file)

## Slide 9
BOME: import mapping file (BMTP file)

## Slide 10
BOME: Aliases

## Slide 11
BOME: Devices
Confirm the devices are OPEN!
Ensure ONLY these 2x options are checked:
- “From Traktor” -> device 1 in OPEN - “to DDJ” -> DDJ-1000 OPEN
Confirm it looks EXACTLY like on the picture
Confirm this “cross” on EXACTLY these aliases

## Slide 12
Step #3
MAP FOR BOM: VERIFICATION
do not skip any step!

## Slide 13
BOME VERIFICATION STEPS:
  Confirm the “Bome MIDI Translator 1” device is created (longformat)
    Method: menu View ; settings ; virtual midi ports ; 1 port; long port names
  Confirm the 4x midi ports were opened correctly
    Method: Click log window; check log
  Confirm that the Controller talks to BOME
    Method: Click log window; click “MIDI-IN/OUT”; Press any button on the controller; confirm they appear in the log file; unclick “MIDI-IN/OUT”
  Confirm that the BOME clock is running
    Method: Click log window; click “rules”; see a lot of messages appearing
    unclick “rules” to stop loggin
  Minimize BOME to keep it running

## Slide 14
BOME settings: auto start with windows
Auto start with Windows!

## Slide 15
BOME settings: long port name device
Long port names!

## Slide 16
BOME: Correct startup log
4x messages here!
Do not change this! Default is ONLY - “From Traktor” OPEN - “to DDJ” OPEN confirm devices are OPEN!
Do not change this “cross”!

## Slide 17
BOME: confirm DDJ talks to BOME
Pressing and releasing any button generates 4 log lines. This is always in the DDJ->BMT1 direction
Activate MIDI debug here

## Slide 18
BOME: confirm internal clock
HZ goes up one by one continuously
Activate rules debug here
(Please click “rules” again to stop the logging)
Tip!

## Slide 19
Step #4
MAP FOR TRAKTOR: INSTALLATION do not skip any step!

## Slide 20
CREATE A BACKUP:
  Note: the mapping replaces a lot of your settings. In any cases, Traktor always makes automatic backups in “Root_Dir\Backup\Settings”
  Open Traktor
  Click Settings
  Click big “export button” on lower left corner
  Ensure all settings are clicked
  Save the file
INSTALL TRAKTOR MAPPING:
  Click Settings
  Click big “import button” on lower left corner
  Accept all checks; PLUS additionally click the “Audio device settings”
INSTALL TRAKTOR MAPPING (second time):
  Repeat above process a second time. This is only to avoid a Traktor bug that gets the FX list wrong.
Extra click

## Slide 21
TRAKTOR: create backup of your settings
Backup everything!

## Slide 22
TRAKTOR: import mapping

## Slide 23
TRAKTOR: click audio device config
Please include this one as well

## Slide 24
TRAKTOR: import mapping (second time)

## Slide 25
Step #5
MAP FOR TRAKTOR: VERIFICATION do not skip any step!

## Slide 26
TRAKTOR VERIFICATION:
  Note: the Preferences window is now quite slow to open. This is another Traktor bug.
  Confirm the audio device is “DDJ-1000 ASIO”
    Method: Settings ; audio setup ; confirm audio device
  Confirm the Output routing
    Method: Settings ; output routing; confirm “internal”; confirm “3 / 4 / 1 / 2”
  Confirm that all 6x pages have exactly “Bome Midi Translator1”
    Method: Settings; controller manager; click each of the 6x pages one-by-one; check IN and OUT port
    DO NOT CHANGE TO DDJ-1000 in the controller manager!!!
    DO NOT FORGET TO CONFIRM ALL 6x PAGES!
  Verify that sound is played
    Method: Load a track; click Cue and play/pause repeatedly
    Use shift+quantize to send a reset command to BOME
  Verify that BOME sees all the messages
    Method: open the bome window; click the “CUE” button; verify that the BOME log displays at least 8x log lines per human click
Beware #1!
Beware #2!

## Slide 27
TRAKTOR: check audio device

## Slide 28
TRAKTOR: check output routing
Configure your channels with 3 / 4 / 1 / 2

## Slide 29
TRAKTOR: how to record Traktor + CDJs

## Slide 30
TRAKTOR: check MIDI device is long format
Both IN and OUT = Long format For ALL 6 PAGES!
first click here

## Slide 31
BOME: confirm bidirectional flow
Pressing and releasing any button generates at least 8x log lines. This is both in the DDJ->BMT1 direction and the BMT1->DDJ direction
Stop “rules” log

## Slide 32
In my experience there is no need to set the unit to forced MIDI mode.
If this is ever necessary, instructions are on page 26 of the DDJ-1000 manual:
no USB cable
power off DDJ
Press left play + left shift + turn on DDJ
left Slip Reverse:
  Off = auto mode
  ON = forced mode
Power off DDJ
Power ON DDJ
insert USB cable.
DDJ-1000: forced MIDI mode

## Slide 33
TRAKTOR DJ Software
BOME MIDI Translator
DDJ-1000
OS Driver
AUDIO path
BMTP file (7 presets)
TSI FILE (6 sub pages)
MIDI path
BMTS file
Settings
USB
in port
out port
From Traktor
BMT1
DDJ-1000
To Traktor
From DDJ
To DDJ

## Slide 34
IF ITS STILL NOT WORKING #1
Re-confirm you have BOME in the macOS accessibly security.
Re-confirm you have “Bome midi Translator 1” on all 6x pages in Traktor.
Re-confirm the DDJ-1000 is the audio device and your output/input routing.
Re-confirme Rekordbox performance mode works.

## Slide 35
IF ITS STILL NOT WORKING #2
Make a HD video of the verification steps, INCLUDING THE BOME LOG.
Put your phone really close to the screen for me to read the small text!
Upload the video to https://wetransfer.com and send an email to pedro.estrela@gmail.com

## Slide 36
ANNEX: DDJ-800

## Slide 37
ANNEX: XDJ-XZ