## Slide 1
DDJ-1000 BOME mapping installation for Traktor
(from version 6.7.0 and newer: now also applicable to all DDJ controllers [SX2/SZ/SRT/etc]. See Annexes for specific instructions!)
This mapping requires the “BOME Midi translator Pro” third-party software. A free trial is available. Do not skip any step!
See also the FAQ in a separate pdf file, and the “gotchas” on page 34.

## Slide 2
Step #0
CONFIRM THAT REKORDBOX PERFORMANCE MODE WORKS PROPERLY IN YOUR SYSTEM!!
Driver Download: https://www.pioneerdj.com/en/support/software/controller/ddj-1000/#drivers
Firmware download: https://www.pioneerdj.com/en/support/software/controller/ddj-1000/#firmware-update
Rekordbox DJ download: https://rekordbox.com/en/
VirtualDJ Instructions (for reference): https://www.virtualdj.com/manuals/hardware/pioneer/ddj1000/installation.html

## Slide 3
Step #1
BOME TRIAL: INSTALLATION do not skip any step!

## Slide 4
BOME SOFTWARE INSTALLATION:
  Download and install the BOME trial from https://www.bome.com/products/miditranslator#downloads
MAC-OS SECURITY ENABLE (see page 40 of the BOME manual):
  macOS 10.9 and later:
    System Preferences → Security & Privacy → Privacy → Accessibility -> Add “BOME”
  macOS 10.8 and earlier:
    System Preferences → Universal Access → check 'access for assistive devices‘
  More info: https://www.maketecheasier.com/macos-security-privacy-permissions/

## Slide 5
macOS security:

## Slide 6
Step #2
MAP FOR BOME: INSTALLATION do not skip any step!

## Slide 7
PRELIMINARIES:
  Stop Rekordbox
  Stop Traktor
  Expand all files in the zip file
  Connect the USB cable
  Turn on your DDJ-1000
INSTALLING BOME MAPPING:
  Open BOME. DO NOT RUN TRAKTOR!
  Settings: Import the settings file
    Method: menu View; settings; export/import; import; select BMTS file
  Mapping: load the mapping file
    Method: Click menu File; Open; select BMTP file
  Do not mix up the Settings file with the Mapping file!
Beware!

## Slide 8
BOME: import settings file (BMTS file)

## Slide 9
BOME: import mapping file (BMTP file)

## Slide 10
BOME: Aliases

## Slide 11
BOME: Devices
Confirm the devices are OPEN!
Ensure ONLY these 2x options are checked:
- “From Traktor” -> device 1 in OPEN - “to DDJ” -> DDJ-1000 OPEN
Confirm it looks EXACTLY like on the picture
Confirm this “cross” on EXACTLY these aliases

## Slide 12
Step #3
MAP FOR BOM: VERIFICATION
do not skip any step!

## Slide 13
BOME VERIFICATION STEPS:
  Confirm the “Bome MIDI Translator 1” device is created (longformat)
    Method: menu View ; settings ; virtual midi ports ; 1 port; long port names
  Confirm the 4x midi ports were opened correctly
    Method: Click log window; check log
  Confirm that the Controller talks to BOME
    Method: Click log window; click “MIDI-IN/OUT”; Press any button on the controller; confirm they appear in the log file; unclick “MIDI-IN/OUT”
  Confirm that the BOME clock is running
    Method: Click log window; click “rules”; see a lot of messages appearing
    unclick “rules” to stop loggin
  Minimize BOME to keep it running

## Slide 14
BOME settings: auto start with windows
Auto start with Windows!

## Slide 15
BOME settings: long port name device
Long port names!

## Slide 16
BOME: Correct startup log
4x messages here!
Do not change this! Default is ONLY - “From Traktor” OPEN - “to DDJ” OPEN confirm devices are OPEN!
Do not change this “cross”!

## Slide 17
BOME: confirm DDJ talks to BOME
Pressing and releasing any button generates 4 log lines. This is always in the DDJ->BMT1 direction
Activate MIDI debug here

## Slide 18
BOME: confirm internal clock
HZ goes up one by one continuously
Activate rules debug here
(Please click “rules” again to stop the logging)
Tip!

## Slide 19
Step #4
MAP FOR TRAKTOR: INSTALLATION do not skip any step!

## Slide 20
CREATE A BACKUP:
  Note: the mapping replaces a lot of your settings. In any cases, Traktor always makes automatic backups in “Root_Dir\Backup\Settings”
  Open Traktor
  Click Settings
  Click big “export button” on lower left corner
  Ensure all settings are clicked
  Save the file
INSTALL TRAKTOR MAPPING:
  Click Settings
  Click big “import button” on lower left corner
  Accept all checks; PLUS additionally click the “Audio device settings”
INSTALL TRAKTOR MAPPING (second time):
  Repeat above process a second time. This is only to avoid a Traktor bug that gets the FX list wrong.
MAC-OS AUDIO OUTPUT ROUTING:
  Set preferences / Output Routing / Internal to: 2 / 3 / 0 / 1
Extra click!

## Slide 21
TRAKTOR: create backup of your settings
Backup everything!

## Slide 22
TRAKTOR: import mapping

## Slide 23
TRAKTOR: click audio device config
Please include this one as well

## Slide 24
TRAKTOR: import mapping (second time)

## Slide 25
Step #5
MAP FOR TRAKTOR: VERIFICATION do not skip any step!

## Slide 26
TRAKTOR VERIFICATION:
  Note: the Preferences window is now quite slow to open. This is another Traktor bug.
  Confirm the audio device is “DDJ-1000 ASIO”
    Method: Settings ; audio setup ; confirm audio device
  Confirm the Output routing
    Method: Settings ; output routing; confirm “internal”; confirm “3 / 4 / 1 / 2”
  Confirm that all 6x pages have exactly “Bome Midi Translator1”
    Method: Settings; controller manager; click each of the 6x pages one-by-one; check IN and OUT port
    DO NOT CHANGE TO DDJ-1000 in the controller manager!!!
    DO NOT FORGET TO CONFIRM ALL 6x PAGES!
  Verify that sound is played
    Method: Load a track; click Cue and play/pause repeatedly
    Use shift+quantize to send a reset command to BOME
  Verify that BOME sees all the messages
    Method: open the bome window; click the “CUE” button; verify that the BOME log displays at least 8x log lines per human click
Beware #1!
Beware #2!

## Slide 27
TRAKTOR: check audio device

## Slide 28
TRAKTOR: check output routing
Windows: channels are 3 / 4 / 1 / 2
Windows: channels are 2 / 3 / 0 / 1

## Slide 29
TRAKTOR: recording settings

## Slide 30
TRAKTOR: check MIDI device is long format
Both IN and OUT = Long format For ALL 6 PAGES!
first click here

## Slide 31
BOME: confirm bidirectional flow
Pressing and releasing any button generates at least 8x log lines. This is both in the DDJ->BMT1 direction and the BMT1->DDJ direction
Stop “rules” log

## Slide 32
Step #6
PROPER START SEQUENCE

## Slide 33
PROPER START-UP SEQUENCE IF YOU HAVE PROBLEMS:
  Stop everything
  Start Laptop
  Start DDJ-1000
  Start BOME
  Start Traktor

## Slide 34
IF ITS STILL NOT WORKING #1
Audio doesn’t work:
Re-confirm the DDJ-1000 is your audio device
Re-confirm output routing is 3/4/1/2 in windows and 2/3/0/1 in macOS
Re-confirm Rekordbox performance mode works.
Audio works - but MIDI doesn’t :
Re-confirm you have BOME in the macOS accessibly security
Re-confirm you have “Bome midi Translator 1” on all 6x pages in Traktor
MIDI works but jog screens / Leds doesn’t :
Reset the jog Screens using shift+quantize
Start components in this order: #1 Laptop #2 DDJ #3 BOME #4 Traktor

## Slide 35
IF ITS STILL NOT WORKING #2
Make a HD video of the verification steps, INCLUDING THE BOME LOG.
Put your phone really close to the screen for me to read the small text!
Upload the video to https://wetransfer.com and send an email to pedro.estrela@gmail.com

## Slide 36
ANNEXES

## Slide 37
In my experience there is no need to set the unit to forced MIDI mode.
If this is ever necessary, instructions are on page 26 of the DDJ-1000 manual:
no USB cable
power off DDJ
Press left play + left shift + turn on DDJ
left Slip Reverse:
  Off = auto mode
  ON = forced mode
Power off DDJ
Power ON DDJ
insert USB cable.
DDJ-1000: forced MIDI mode

## Slide 38
TRAKTOR DJ Software
BOME MIDI Translator
DDJ-1000
OS Driver
AUDIO path
BMTP file (7 presets)
TSI FILE (6 sub pages)
MIDI path
BMTS file
Settings
USB
in port
out port
From Traktor
BMT1
DDJ-1000
To Traktor
From DDJ
To DDJ

## Slide 39
ANNEX: DDJ-800

## Slide 40
ANNEX: XDJ-XZ

## Slide 41
DDJ-1000SRT specific instructions for the Traktor mapping (for v6.1.X – not yet updated to V6.7.0 BOME)
Please use the specific TSI for the DDJ-1000SRT. This is the same mapping as the DDJ-SZ mapping, but with small customizations to make it work well on the SRT:
Jog screens are NOT supported. This is because they are not documented on the Pioneer MIDI map file. Please request this in https://serato.com/forum/discussion/1736390
Please put your jog weight to “heavy”
  This will significantly improve scratching and jogFX
Audio device in external mode.
  This means that ALL the pioneer effects (both colorFX and beatFX work for USB sources
  See next slides for config
Please avoid VINYL OFF mode. The TSI disables jog touch in this case, but the jog loses resolution compared to VINYL ON mode
Beatjump buttons added. Please use shift+IN/OUT to configure the loop size (=jump size)
BeatFX ON/OFF is now for pioneer beatFX only
Automatic layout changing was removed
ANNEX: DDJ-1000SRT

## Slide 42
ANNEX: DDJ-1000SRT
(note: pictures are for v6.1.X; v6.7.0 will also work, but was not tested yet)

## Slide 43
ANNEX: DDJ-SZ
SET PREVIEW TO
SAME VALUES
AS DECK 4!

## Slide 44
ANNEX: DDJ-SX3
SET PREVIEW TO
SAME VALUES
AS DECK 4!
(Select SX3 device here)
(Select SX3 device here)

## Slide 45
ANNEX: DDJ-SX2
(Put SX2 channels here)
(Select SX2 device here)