## Slide 1
DDJ-1000 Traktor mapping installation
This work requires the “BOME Midi translator Pro” third-party software
Steps are first explained in a single page, then followed by detailed screenshots
Do not skip any step!
See also the installation FAQ (this a separate pdf file)

## Slide 2
Step #0
CONFIRM THAT REKORDBOX DJ WORKS IN YOUR SYSTEM!
Driver Download: https://www.pioneerdj.com/en/support/software/controller/ddj-1000/#drivers
Firmware download: https://www.pioneerdj.com/en/support/software/controller/ddj-1000/#firmware-update
Rekordbox DJ download: https://rekordbox.com/en/

## Slide 3
TRAKTOR DJ Software
BOME MIDI Translator
DDJ-1000
OS Driver
AUDIO path
BMTP file (7 presets)
TSI FILE (6 sub pages)
MIDI path
BMTS file
Settings
USB
in port
out port
From Traktor
BMT1
DDJ-1000
To Traktor
From DDJ
To DDJ

## Slide 4
Step #1
BOME-MAP INSTALLATION do not skip any step!

## Slide 5
PRELIMINARIES:
  Stop Rekordbox
  Stop Traktor
  Expand all files in the zip file
  Connect the USB cable
  Turn on your DDJ-1000.
  Download and Install the BOME trial from https://www.bome.com/products/miditranslator#downloads
INSTALLING BOME MAPPING:
  Open BOME. DO NOT RUN TRAKTOR!
  Settings: Import the settings file
    Method: menu View; settings; export/import; import; select BMTS file
  Mapping: load the mapping file
    Method: Click menu File; Open; select BMTP file
  Do not mix up the Settings file with the Mapping file!
Beware!

## Slide 6
BOME: import settings file (BMTS file)

## Slide 7
BOME: import mapping file (BMTP file)

## Slide 8
BOME: Devices
confirm the devices are OPEN!
Default is ONLY : - “From Traktor” OPEN - “to DDJ” OPEN
If you have problems here confirm tat Rekordbox Performance works in your system

## Slide 9
BOME: Aliases

## Slide 10
Step #2
BOME-MAP VERIFICATION
do not skip any step!

## Slide 11
BOME VERIFICATION:
  Confirm the BMT1 device is created (short format)
    Method: menu View ; settings ; virtual midi ports ; 1 port; short port names
  Confirm 4x midi ports are opened correctly
    Method: Click log window; check log
  Confirm DDJ talks to BOME
    Method: Click log window; click “MIDI-IN/OUT”; Press any button on the controller; confirm they appear in the log file; unclick “MIDI-IN/OUT”
  Confirm the BOME clock is running
    Method: Click log window; click “rules”; see lots of messages flowing; unclick “rules”
  Minimize BOME to keep it running

## Slide 12
BOME settings: auto start with windows
Auto start with Windows!

## Slide 13
BOME settings: device “BMT1”
Short port names!

## Slide 14
BOME: Correct startup log
4x messages here!
Do not change this! Default is ONLY - “From Traktor” OPEN - “to DDJ” OPEN confirm devices are OPEN!
Do not change this “cross”!

## Slide 15
BOME: confirm DDJ talks to BOME
Pressing and releasing any button generates 4 log lines. This is always in the DDJ->BMT1 direction
Activate MIDI debug here

## Slide 16
BOME: confirm internal clock
HZ goes up one by one continuously
Activate rules debug here
(Please click “rules” again to stop the logging)
Tip!

## Slide 17
Step #3
TRAKTOR-MAP INSTALLATION do not skip any step!

## Slide 18
INSTALL TRAKTOR MAPPING:
  Open Traktor
  Click Settings
  Click big “import button” on lower left corner
  Accept all check settings, PLUS additionally the “Audio device settings”
  Repeat the mapping installation a second time.
    This is only requires to confirm the FX list is correct
    (this is a Traktor bug that is going on for years)!

## Slide 19
TRAKTOR: import mapping

## Slide 20
TRAKTOR: add audio device config
Please include this one

## Slide 21
TRAKTOR: import mapping (second time)

## Slide 22
TRAKTOR: add audio device config (second time)
Please include this one

## Slide 23
Step #4
TRAKTOR-MAP VERIFICATION do not skip any step!

## Slide 24
TRAKTOR VERIFICATION:
  Note: the Preferences window is now quite slow to open. This is a known Traktor bug.
  Confirm the audio device is “DDJ-1000 ASIO”
    Method: Settings ; audio setup ; confirm audio device
  Confirm that all 6x pages have exactly “BMT1”
    Method: Settings; controller manager; click each of the 6x pages one-by-one; check IN and OUT port
    DO NOT SET DDJ-1000 in the controller manager!!!
    DO NOT FORGET TO CONFIRM ALL 6x PAGES
  Verify that sound is played
    Method: Load a track; click Cue and play/pause repeatedly
    Use shift+quantize to send a reset command to BOME
  Verify that BOME sees all the messages
    Method: open the bome window; click the “CUE” button; verify that the BOME log displays at least 8x log lines per human click
#1 problem!!
#2 problem!!

## Slide 25
TRAKTOR: check audio device

## Slide 26
TRAKTOR: MIDI via “BMT1”
Both IN and OUT = “BMT1”
For ALL 6 PAGES!

## Slide 27
TRAKTOR: MIDI via “BMT1”
ALL 6 PAGES WITH BMT1!

## Slide 28
BOME: confirm bidirectional flow
Pressing and releasing any button generates at least 8x log lines. This is both in the DDJ->BMT1 direction and the BMT1->DDJ direction
Stop “rules” log

## Slide 29
IF ITS STILL NOT WORKING #1
Do the reboot and confirm you have shortports (“BMT1”) in all 6 pages. If still having long ports, set “Bome midi Translator” manually to all 6 pages

## Slide 30
IF ITS STILL NOT WORKING #2
Make a HD video of the verification steps, INCLUDING THE BOME LOG.
Upload the video to https://wetransfer.com so that I can read the small text Send an email to pedro.estrela@gmail.com